## Slide 1: SolSight
Solder Defect Detection System — Automatic Optical Inspection with AI AI-Powered Defect Detection

## Slide 2
SolSight
Solder Defect Detection System
Unsupervised Anomaly Detection for PCB Assembly
block body
Fully Convolutional Autoencoder for real-time inspection
Resolution-Agnostic architecture (16px to 160px)
Zero-Supervised learning on defect-free joints
The Problem
Manual solder joint inspection is time-consuming & error-prone
Defects & degradation in PCB assemblies directly impact reliability
Traditional AOI systems require extensive labeled datasets
Defect variations across hardware make generalization difficult
What if we could detect anomalies without labeling defects?
Our Solution
Train on Normal Joints Detect Anomalies as Reconstruction Failures
Architecture Design
Fully Convolutional Autoencoder (CAE)
Encoder: 3 convolutional layers with stride Bottleneck
Decoder: 3 transpose convolutions with stride Reconstruction
Scoring: Adaptive SSIM window scaled for patch size
Multi-Scale Training Strategy
Key Advantage: Single model handles patches from 16px to 160px natively
No patch rescaling needed
Adaptive SSIM window calibration per resolution
Trained on 5,700+ procedurally synthesized patches
Synthetic Benchmark Results
Key Insight: Model generalizes exceptionally well to untrained resolutions
Cold joint detection: 96–100% recall across all tiers
Per-tier thresholds enable resolution-aware scoring
Real-World PCBA Results (SolDef-AI) Zero-Shot Transfer to Physical Hardware
Production-ready for site-specific calibration workflows
Empirical Failure Boundaries
Validated across resolution tiers
Per-tier adaptive thresholding addresses boundary cases
Stress test suite verifies reliability margins
Deployment Workflow
Calibration Phase
  Collect 100–200 site-specific good solder samples
  Fine-tune threshold on local hardware ()
Inference Deployment
  Stream patches into model via camera feed
  Generate anomaly scores in real-time (ms per patch)
  Visualize DSSIM heatmaps for operator review
Continuous Monitoring
  Track false positive / false negative rates
  Trigger alerts on batch degradation
Why SolSight?
No labeled defect data needed. Deploy on day one.
Technical Stack
Language: Python 3.10+
Deep Learning: PyTorch 2.1+
Vision: OpenCV, scikit-image (SSIM, morphology)
Metrics: ROC-AUC, AUROC, precision/recall
Deployment: ONNX export for edge hardware (optional)
Fully open-source MIT License Production-validated
Quick Start (3 Steps) Step 1: Setup
git clone https://github.com/stanmaluki/SolderDefectDetectionSystem cd SolderDefectDetectionSystem && pip install -r requirements.txt
Step 2: Verify Architecture
python scripts/shape_check.py
Step 3: Run Evaluation
python scripts/evaluate.py # Full benchmark python src/inference/predict.py # Single patch inference
Key Metrics Summary
Training Time: 30 epochs on 5,700 patches @ 32 batch size
Inference Speed: ms per patch (CPU-capable)
Model Size: 2.4 MB (deployable on edge devices)
Memory: 280 MB GPU (or CPU-compatible)
Use Cases & Applications
High-Volume Manufacturing
  Real-time PCB assembly line defect screening
  Zero downtime for model retraining
Quality Assurance
  Batch-level anomaly tracking and reporting
  Automated defect triage and operator alerts
Research & Development
  Benchmark new soldering processes against baseline normals
  Rapid failure analysis without labeled datasets
Future Enhancements
Multi-Modal Fusion
  Combine visible + thermal imaging for enhanced detection
Online Adaptation
  Continuous threshold refinement with human feedback loop
Edge Deployment
  ONNX + TVM quantization for ARM/FPGA targets
Explainability Layer
  Attention maps and gradient-based defect importance ranking
Contact & Resources
GitHub Repository
github.com/stanmaluki/SolderDefectDetectionSystem
Documentation
Full evaluation guide, architecture specs, and failure boundaries
License
MIT — Free for research and commercial use
Questions?
Automatic Optical Inspection
Made Simple & Unsupervised
AI-Powered Quality Control